BMCS Shear Zone Tasks

Software design

- set the model ShearZone into the structure of the BMCS Simulator

- separate the material model class and the class for cross sectional design from the simulator

- handle the state changes, reactivate properties (input_change, state_change)

Model infrastructure – evaluation of secondary state variables

- define evaluation of the dissipated energy along with the load – displacement curve

- use the energy dissipation to propose regularization criteria of the problem

- consistently distribute the global shear force along the ligameent including the
continuum consideration in the uncracked part / mixed mode propagation criterion / the shear and decohesion at the crack tip / dowel effect

- test if the derivatives with respect to the primary unknowns (x_rot_z and theta) can be constructed for the residuum equations

- improve the stress shape functions – currently just midpoint integration within each segment – insufficient in the fracture propagation segment.

Crack propagation criterion

- improve the quality of the local stress representation at the crack tip

- integrate the mixed-mode propagation criteria – Bazant/Planas – Page 98

- search for further available analytically prefabricated criteria (Meschke, Dummsdorf ??)

Plotting

- cluster the plot methods for individual variables to show concise information in each diagram, e.g. Load / Displacement along the Fracture energy